## Slide 1
Y. K. Rao
M/s Coroney Technologies Pvt. Ltd.
Vadodara (Gujarat) yk.rao@coroney.com
+91 -9601351464
Presentation on
Suggested Technology for
Remediation of Contaminated Soil

## Slide 2: Technology Proposed: Based on High Vacuum, Low Temperature Thermal Desorption Process
Salient Features:
Targeted Mercury levels in treated soil can be achieved even up to 6 mg/kg in an environmentally sound and efficient manner.
Process is dry. There are No emissions in air and water. Complete system is Electronic Controlled with minimum of a operator interference.
Dust separation before condensers. No water washing / No filter press/ No water contamination with mercury with ZLD approach.
No Mercury emissions from into vacuum pumps &/or from vacuum pump as exhaust metallic Hg can be recovered, or converted to solid non hazardous waste which can be disposed in land fill at TSDF.
Final material balancing per weight input to weight output can be achieved.
Occupational safety & health issued are adequately addressed.

## Slide 3
Proposed Technology - Process Flow Diagram *

## Slide 5: Proposed Technology comparison with other Technology
Parameters | Other Technology | Proposed Technology
Temperature | Very High (450 O C) * | Low ( <310 oC )
Vacuum | POOR More than 100 mm Hg | HIGH less Than 5 mm Hg
Dust separation | Mechanical Vapor filters | Vacuum Ionization
Vacuum Pressure drop | 5- 20 mm Hg | 5- 10 Micron
Particle efficiency | 5 micron or above | 0.3 Micron
Scrubbing | Oil scrubbing * | NO Scrubbing
Air pollution control | Carbon filter exhaust of Vacuum pumps. The separation poor | VACULIFE before Vacuum pump The Mercury vapors separation efficiency is more than 98%

## Slide 6
Parameters | Other Technology | Proposed Technology
Mercury collected as Liquid mercury | 0 % Because Hg mixes with oil , water ,VOC , or in activated Carbon | 75 % - 90 % (Material Balancing)
Water washing | Required | NOT required
Energy | High | Less by 30- 50 %
Cycle time | High | Less by 35- 55 %
Technology | Imported | Indigenous / Innovative
Proposed Technology comparison with other Technology

## Slide 7: SALIENT FEATURES OF SOIL REMEDIATION USING THERMO / HIGH VACUUM PROCESS COUPLED WITH USHASH TM & VACULIFE TM
Description | Proposed
Level of Vacuum & PROCESS Temperature | High 5 mm Hg & <310 Deg C
MECHANICAL FILTERS & CARTRIDGE FILTERS | Not required
Hazardous elements separation from Gas stream | Vacuum ionization to charge & trap solid, liquid,
SOIL WATER WASHING | Not required
Escaped dust particles separation . | With USHASH TM to prevent clogging of condensers rest with VACULIFE filters ..
Carbon Filters on exhaust of Vacuum pumps . | Not required **
effluent water disposal for given soil | Close to zero emission

## Slide 8: SALIENT FEATURES OF SOIL REMEDIATION USING THERMO / HIGH VACUUM PROCESS COUPLED WITH USHASH TM & VACULIFE TM
Description | Proposed
Heating | Indirect heating with thermic oil
Mercury emissions in air | Below detection limit with se of VACULIFE filters .
Solid carbon disposal | Not required.
Effluent water treatment | Minimum requirement, effluent being soft.
Energy cost | Low energy cost. 35- 55 % less in comparison with others.
Environmental Friendly Technology | Yes. UNIQUE and TWIN Patents with ZLD approach

## Slide 9: WAY FORWARD ( Hg soil remediation)
Considering the fact that mercury is highly hazardous and toxic in nature the remediation process must be targeted with zero emissions / zero discharge approach. This is possible to a great extent with the use of Vacuum thermal desorption process for soil remediation and proper dust separation system thereof.
Usage of water in the total process should be limited only for Condenser / equipment cooling .
It should be preferred that the reclaimed mercury is either reusable or treated suitably for safe disposal in land fill at TSDF as per Rules.

## Slide 10: Remediation without & with washing
DESCRIPTION | Remediation without WAHSING | Remediation with WAHSING
water treatment Plant capacity | Small Plant is required to treat and dispose water safely | Bigger Plant size is required
Quantity of soil to be remediated | Quantity of soil to be remediated is little higher | Less. This was mere failure in KODAIKANAL . Mercury Balancing is to be achieved in washing .
Handling of SOIL | It is easy | Very difficult because soil is wet and Mud
Mercury contamination in AIR wash area | doesn’t exist | Exists because Mercury starts boiling from 18 Deg C
Water disposal with Hg | doesn’t exist | Exists
Mercury traces in surrounding area of air in soil handling equipment | doesn’t exist | Exists
Heat required to remediate soil / MT | Less By 60 % | High because water latent heat is more than soil **
Time Required to remediate soil / MT | Less by 40 – 50 % | Very High
Mass Balancing of Mercury in soil remediation | Very much possible | Not possible . Because KODAIKANAL soil remediation actual mercury collected in process is ZERO Gram
AIR Pollution | Negligible / BDL with proper care umps | High Because all wash area exposed to Air causes alarming Hg levels